## Slide 1: POC Procedures Working Group Discussion Topics
3-4 February 2016

## Slide 2: Topics
Type 4 Meter Identification
Type 4 Metrology Requirements
Distributor Sample Metering
Network Device Management Requirements
Reconnection, Disconnection
  Site Identifier
  Provision of Services
  NMI Status
Emergency Priority Procedures
Meter Churn

## Slide 3: 1. Type 4 Meter Identification

## Slide 4: Type 4 – Meter Identification Background
Under the NER from 1 December 2017, a Type 4 metering installation will be one of the following:
“EXISTING” Type 4 metering installation (installed before or after 1 Dec 2017 for large customers),
“LEGACY” Type 4 metering installation (installed prior to 1 Dec 2017 for a small customer), or
“ADVANCED” Type 4 metering installation that meets minimum services specification (installed after 1 Dec 2017 for a small customer).
A Type 4A meter (defined under rule 7.8.4) is a manually read variant of a Type 4 meter. A Type 4A meter can only be installed where:
AEMO exempts the Metering Coordinator from complying with the requirement to install a Type 4 meter (clause 7.8.3(a)) where the Metering Coordinator demonstrates to AEMO's reasonable satisfaction that there is no existing telecommunications network which enables remote access to the metering installation at that connection point; or
where, in the Metering Coordinator’s reasonable opinion, the small customer has communicated its refusal to the installation or proposed installation of a type 4 metering installation.

## Slide 5: Type 4 – Meter Identification Background 2
Comments made to the AEMC included suggestions that ADVANCED meters should be identified under a specific Type of meter rather than including them under the Type 4 banner, however the AEMC did not agree.
The Rule Determination (RD) page 328 states,
“The Commission does not consider it necessary to include a new meter type in the NER for small customer metering installations. MSATS is sufficiently flexible and can be used to provide information to participants on the services that are available from a particular metering installation without the need to create new meter types in the NER.”
Hence rules will identify just a Type 4 and Type 4A meter and if any further differentiation is necessary, it will need to be considered in AEMO procedures (and systems).

## Slide 6: Type 4 – Meter Identification Context 1
ADVANCED metering installations for small customers installed after 1 Dec 2017 must be capable of supporting the requirements of the minimum services specification (MSS), but EXISTING metering installations need not be capable.
Comparing the new MSS requirements (Table S7.5.1.1) for ADVANCED metering installations with the current metering installation components (7.8.2(a)) confirms that an EXISTING metering installation that meets all the mandatory requirements of clause 7.8.2(a) does not need to support all requirements of the MSS.
EXISTING metering installations do not need to be capable of reactive energy measurement, provision of accumulated metering data at the start and end of a specified period and provision of voltage, current, power and frequency measurement (it is likely that most EXISTING metering installations will have this capability).
Thus it could be argued that the ADVANCED metering installation is the more feature rich.
A LEGACY metering installation, although provided at a small customer metering installation, does not have to and will not necessarily be capable of supporting the minimum services specification.

## Slide 7: Type 4 – Meter Identification Context 2
It is reasonable to consider that these metering installations should be independently identifiable, for reasons including:
Customer transfers
Appointment of Metering Coordinators
Appointment of providers
Compliance management
Accreditation
Type 5 metering installations are likely to share the same validation and substitution requirements, etc. as Type 4A meters.
The Type 4A arrangement is a temporary arrangement whereas Type 5 is a permanent arrangement therefore is appears reasonable that Type 4A and Type 5 would be independently identifiable.

## Slide 8: Type 4 – Meter Identification Context 3
The creation of a code or codes within MSATS could indicate the nature of the metering installation under the Type 4 banner. This could be achieved by:
Using different Metering Installation Type Codes for small and large Type 4 customers (e.g. 4S, 4L), retaining all LEGACY metering installations under the existing Type 4 code until such time as those metering installations are altered.
Do not alter the Type Code (i.e. continue to identify as Type 4 only) and use two new COMMS fields – e.g. 4S, 4L – to indicate the nature of the metering set up*. The procedures could make these codes compulsory.
Type 4A meters could be identified as Type 4 but with the COMMS field indicating a manually read advanced meter. E.g. “MRAM”, “MRAM4A” or “4SMRAM”. Once the meter becomes compliant with the requirements of Type 4, only the COMMS field would change, reflecting the actual change. Alternatively an explicit Metering Installation Type Code of Type 4A could be used.
Both the Metering Installation Type Code and the COMMS field in MSATS support 8 characters including numbers, giving options for adding new codes as indicated.
* e.g. in the Meter Install Code on the Meter Register (Meter) table

## Slide 9: Type 4 – Meter Identification Questions
How to identify Type 4 meters?
  Option 1: Introduce new Metering Installation Type Codes in MSATS to distinguish between the variations of Type 4 and Type 4A meters.
  Option 2: Introduce new COMMS field options and require in the procedures that these be used to uniquely identify the nature of the Type 4 metering installation.
  Other options?
AEMO recommendation - utilise the Metering Installation Type Codes as this field exists, must be populated, and the change only requires an amended range of meter codes.

## Slide 10: 2. Type 4 Metrology Requirements

## Slide 11: Type 4 – Metrology Requirements Background
Metrology requirements for existing Type 4 meters are already in place and detailed.
The Type 4 boundary is unchanged - from 0 to 750 MWh per annum and applicable to small and large customers alike.
The Competition in Metering rule change is expected to result in an increase in the volumes of Type 4 metering installations, particularly for small customers.
Some stakeholders have proposed that there should be a distinction in the Metrology Procedure for large and small customers as a result of the Competition in Metering rule change.
Small customer Type 4 meters will include all of the VIC AMI metering installations which are currently covered under derogation 9.9C of the NER (which expires 1 December 2017) and, today, are registered in MSATS as MRIM metering installations.

## Slide 12: Type 4 – Metrology Requirements Context 1
The procedures must be drafted to comply with the NER.
The NER requires all Type 4 metering installations to have the same metrology requirements.
The NER does not give AEMO specific powers to relax these requirements for a sub-set of Type 4 metering installations.
In the final determination section D5.5 (page 446) the AEMC states:
  “The final rule expands the circumstances in which a Metering Coordinator may alter a type 5 or 6 meter to make it capable of remote acquisition, compared to the draft rule. Specifically, clause 7.8.9(b) of the NER final rule permits the Metering Coordinator, where it is the LNSP, to alter a metering installation where the alteration is reasonably required to enable the LNSP to meet its obligations to provide a safe, reliable and secure network.
  The final rule clarifies the definition of operational difficulties. The final rule also corrects a cross reference in clause 7.10.7(c) that has the effect of clarifying that AEMO may relax or exempt the metering data performance standards associated with a metering installation that is capable of being remotely read where the metering installation has been altered under clause 7.8.9(b) of the NER final rule.”

## Slide 13: Type 4 – Metrology Requirements Context 2
Clause 7.10.7(a) requires that a Metering Coordinator must ensure that metering data is provided to AEMO for all trading intervals where the metering installation has the capability for remote acquisition of metering data, and requires in Clause 7.10.7(a)(4) that the data is provided in accordance with the performance standards specified in the metrology procedure.
Clause 7.10.7(c) allows AEMO to relax or exempt the performance standards specified in Clause 7.10.7(a)(4) in circumstances, including those referred to in clause 7.8.9(b), when AEMO and the Metering Coordinator agree on a lower performance standard that does not place a material risk on AEMO’s ability to meet its settlements and prudential requirements obligations under the Rules.
The only specific circumstances stated in the Rules in which the standards may be relaxed – clause 7.8.9(b) – is when an MC has altered a Type 5 or 6 meter to make it capable of remote acquisition for operational difficulties (e.g. where the meter is on a remote property or in a secure or hazardous environment) or to enable the LNSP to meet its obligations to provide a safe, reliable and secure network.
In summary, to the extent that there are powers to relax performance standards of the metrology procedures this can only be done if AEMO agrees on a lower performance standard that does not place a material risk on its ability to meet the settlement and prudential requirements.

## Slide 14: Type 4 – Metrology Requirements Questions
Can stakeholders provide substantive reasons for modifications of metrology requirements for sub-sets of Type 4 metering installations for AEMO to consider?
What specific modifications do stakeholders suggest?

## Slide 15: 3. Distributor Sample Metering

## Slide 16: Distributor Sample Metering Background
Distributors are required under jurisdictional rules to maintain interval meters to sample the usage of non-interval meter customers to provide data required for profiling.
The specific sampling rules are contained in jurisdictional instruments and are reproduced in the Metrology Procedure Part A (2.6 and 3.4.2) and Part B Section 13.
Metering Competition creates the possibility that a “non-interval” meter customer with sample metering moves to having its metering services provided by a Metering Coordinator other than the DNSP.
This discussion is unrelated to sample meter testing.

## Slide 17: Distributor Sample Metering Questions
Is this a problem?
  If a sample meter is removed, the DNSP installs a new one elsewhere.
  This could happen today, e.g. due to tariff change, or NMI abolishment.
And if there is a problem, how should it be addressed?
  Co-location of meters is possible but only if the tariff applicable to the meter is retained (i.e. if the sampling of data is still relevant to the controlled load profile).
Other options?

## Slide 18: 4. Network Device Management Requirements

## Slide 19: Network Device Management Requirements - Background
Under clause 7.8.6 of the NER, provisions are introduced regarding Network Devices.
Network devices are apparatus or equipment that enables an LNSP to monitor, operate or control the network for the purposes of providing network services, which may include switching devices, measurement equipment and control equipment.
Network Devices could include a range of specifically power system related devices, such as controlled load profile sample meters and Victorian AMI metering installations (under derogation 9.9C).
Procedures must be developed that:
specify when an existing metering installation that is to be replaced by a Metering Coordinator may be a network device
apply when network devices are installed or removed, including the return of the network device to the LNSP; and
apply to notifications to be given in respect of activities which affect network devices or metering installations and the provision of records.
The issue to be explored relates to the first point – specifically how to identify network assets and when they may be a Network Device.

## Slide 20: Network Device Management Requirements - Context
There are provisions under the NER in clause 7.8.6(f) for the Metering Coordinator to remove a network device without the LNSPs consent, e.g. if it is seeking to install a revenue meter but there is inadequate space to do so without removing the network meter.
It appears reasonable for network devices to be removed and returned to the owner in all circumstances where an agreement has been made between the Metering Coordinator and the Local Network Service Provider to do so, or where the network device is not required to monitor, operate or control the network for the purposes of providing network services such as where the network device provides a
control service which has been installed to facilitate the application of a network tariff at the NMI, such as the control of a hot water load, and where that control service is made obsolete as a result of the Meter Churn; and
switching service which has been installed to facilitate the application of a network tariff at the NMI, such as a timeclock, time switch or ripple controller which is used to change the register on a multi-register meter, and that switching service is made obsolete as a result of the Meter Churn.

## Slide 21: Network Device Management Requirements - Questions
Do stakeholders agree with the previous statement?
To avoid confusion, is there a benefit in the Metering Coordinator being able to identify network devices related to the metering installation?
If identification is beneficial, how could it work?
  Option 1 - Require the LNSP to maintain a list that is kept up-to-date and is either published or distributed to Metering Coordinators?
  Option 2 – Identify the devices in MSATS to indicate it is a network device, e.g. by using the ‘additional site info’ field (non-mandatory) to indicate that it is a network device.
  Other options?

## Slide 22: 5. Disconnection & Reconnection

## Slide 23: Reconnection, disconnection site identifier - Background
While not an express requirement of the NER, it has been suggested that there should be an indicator in MSATS as to whether disconnection of a site was performed remotely or physically.

## Slide 24: Reconnection, disconnection site identifier - Context
The suggestion is that such a feature would provide an MSATS user with information useful in deciding how to reconnect a site (e.g. whether it can be done remotely).
But there are practical problems with such a feature:
After a period of time of disconnection a certificate of electrical safety is required, requiring a site visit.
A site that was remotely disconnected can subsequently be physically disconnected (without MSATS necessarily being updated).
There could be communications faults that prevent a remote reconnection, or a meter fault. Both of these would require a visit to site to reconnect.

## Slide 25: Reconnection, disconnection site identifier - Questions
Is there any perceived value in having any such identifier? Noting that:
  The Metering Coordinator will be the party responsible for ensuring any reconnection is performed in accordance with the rule requirements. A requestor of a reconnection could arrange the compliant management of a service in coordination with the Metering Coordinator; and
  Type 5 and 6 metering installations cannot be remotely disconnected
How would requestors use such an identifier if it did exist?
Why would an identifier in market systems be a more optimal solution than requiring commercially contracted service providers to manage a compliant and efficient service outcome?

## Slide 26: Reconnection, disconnection Provision of Services - Context
Party who can perform the remote energisation services:
The MP is accredited to provide, install and maintain the metering installation.
The MDP is accredited to collect, process and deliver metering data.
AEMO expects that the MP will be the party who’s accreditation will be reviewed to determine the inclusion of any requirements for the performance of remote energisation services
AEMO consider that it would be appropriate for the MDP to take a meter reading immediately prior to a remote disconnection.

## Slide 27: Reconnection, disconnection Provision of Services - Questions
What are stakeholder views on
  Who performs remote services?
  Meter reading requirements with respect to remote disconnection?

## Slide 28: Reconnection, disconnection NMI Status - Context
As an MC’s appointed provider can now perform remote disconnection/reconnection, it is reasonable to consider that they should be able to update the NMI status in MSATS.
Currently only the LNSP can initiate CR505X to update the NMI status. This will need to change to allow the appointed provider to initiate a CR505X to update the NMI status when they perform the remote re-energisation / de-energisation.

## Slide 29: Reconnection, disconnection NMI Status - Questions
What are stakeholder views on updating of NMI Status in MSATS?

## Slide 30: 5. Emergency Priority Procedures

## Slide 31: Emergency Priority Procedures Questions
What could be considered as the criteria for determining when an emergency condition in present for the purposes of the Emergency Priority Procedure under clause 7.8.5 of the NER?
Natural disasters (e.g. fire, flood)?
The number of customers affected?
How are impacted Metering Installations identified?
How is notification of beginning and end of emergency event provided?
And by whom?
Which services are required to assist in management of an emergency event?
Which services are to be prioritised to ensure safety and prevent congestion of request for metering services?
What is a service prioritisation request?

## Slide 32: 5. Meter Churn

## Slide 33: Meter Churn Background
Today the meter churn procedures just cover the FRMP. In the future the procedures must cover MC, MP and MDP and FMRP.
Once triggered, the process for performing meter churn and the contents of communications is not changed under the amended NER.
The process for triggering meter churn has changed, in particular in relation to the current ability for the FRMP to notify the responsible person (RP) for a type 5 or 6 metering installation that it intends to change the meter to a Type 1-4 and become the RP – as described under the previous NER 7.3.4.
Under the amended NER from 1 December 2017, the Metering Coordinator initiates meter churn. For example, a Metering Coordinator may do this:
to ensure compliance with the NER; and
to meet the requirements of contractual relationships with retailers or large customers.

## Slide 34: Next Session

## Slide 35: Topics for Session 2
MSATS requirements
  Case by case review of objection codes
    Still relevant today (and after NER changes)?
    Correctly defined?
    Appropriate objection period?
    Need for new codes?
B2B requirements
  Life support
  Retailer planned interruption
  ROLR requirements
  MC appointment